## Slide 1: Q-ENGINE: Quantum PCA for Intelligent Engine Health Monitoring
A MATLAB-based quantum machine learning framework for dimensionality reduction and degradation detection
Notes: Introduce the project in one line: we use quantum PCA, simulated in MATLAB, to turn many engine sensor readings into one health score that tells us when an engine starts to degrade.

## Slide 2: Engines fail gradually, but 21 sensors hide the trend
An aircraft engine reports temperature, pressure, speed and flow readings every cycle. Degradation shows up as a small drift spread across many of them, buried in noise.
The question
How do we tell that an engine is moving away from normal behaviour before it fails?
Too many signals
21 sensors per engine cycle; watching each one separately does not scale.
Noisy readings
Cycle-to-cycle noise is as large as the early degradation trend.
Late warnings cost
A fault seen only near failure leaves no time to plan maintenance.
Notes: A turbofan engine is monitored by many sensors: temperatures, pressures, shaft speeds, flow ratios. No single sensor says 'this engine is degrading'. The drift is small, noisy and spread over many channels. Maintenance teams need one early, reliable signal. That is the problem this project addresses.

## Slide 3: Our approach: compress, then measure drift
Sensor data
14 informative sensors per cycle
qPCA
finds the dominant patterns
Reduced space
14 sensors become k = 3 components
Anomaly score
distance from healthy behaviour
Engine health
normal, degrading or alert
What makes it more than "we implemented qPCA"
It combines a quantum algorithm, a machine-learning task, a real engineering problem and a usable application, and it measures quantum against classical instead of claiming an advantage.
Notes: The whole project in one picture. Sensor data goes in. qPCA finds the few directions that carry most of the variation. Each engine cycle is projected onto those directions. We measure how far the cycle is from the healthy region, turn that into a 0 to 1 score, and report a status. Classical PCA runs alongside as the baseline so the quantum result is measured, not assumed.

## Slide 4: Dataset: NASA C-MAPSS run-to-failure engine records
100
engines in FD001, each run to failure
21
sensors recorded every cycle
14
sensors kept after removing constant channels
80 / 20
engines for fitting / held out for testing
Life of one engine
Healthy
Gradual degradation
Abnormal, then failure
cycle 1
failure
The first 20% of each engine's life defines "healthy". The last 30 cycles before failure are the "failing" class used to score detection.
Notes: C-MAPSS is NASA's simulated turbofan degradation dataset and the standard benchmark for predictive maintenance. Each engine starts healthy and is run until failure. We use subset FD001: one operating condition and one fault mode, which keeps the study clean. Seven of the 21 sensors are constant in FD001 and carry no information, so 14 remain. FD002 and FD004 have six operating regimes and would need per-regime normalisation, so they are out of scope.

## Slide 5: Preparing the data in four steps
1
Select sensors
Drop channels with two or fewer distinct values. FD001 keeps sensors 2, 3, 4, 7, 8, 9, 11, 12, 13, 14, 15, 17, 20, 21.
2
Optional noise
Add Gaussian noise as a percentage of each sensor's spread. Used only in the robustness experiment.
3
Split by engine
First 80% of engines fit the model. The remaining engines are held out for every reported metric.
4
Standardise
Subtract the mean and divide by the standard deviation of the fitting engines, so no sensor dominates.
Notes: Step one removes sensors with two or fewer distinct values. Step two is optional: it adds Gaussian noise for the what-if experiment. Step three splits by engine, not by row, so the test engines are never seen during fitting. Step four standardises each sensor using only the fitting engines' statistics, which avoids information leaking from the test set.

## Slide 6: Classical PCA: the baseline for every result
Covariance matrix
C = XTX / N
X: standardised sensor matrix, N cycles by 14 sensors
Eigen-decomposition
C v = λ v
v: principal component (a weighted mix of sensors)
λ: variance carried by that component
What the app shows
Scree plot
Share of variance per component, and the cumulative total.
Loadings
Which sensors drive each component.
Projection
z = VkTx turns 14 readings into k coordinates.
Notes: PCA finds the directions along which the data varies most. We compute the covariance matrix of the standardised sensors, find its eigenvalues and eigenvectors, and sort them. Each eigenvalue tells how much variance its direction carries. Keeping the top k directions reduces 14 sensors to k numbers per cycle. Everything qPCA produces is compared against this.

## Slide 7: Quantum PCA: covariance becomes a quantum state
STEP 1
ρ = C / tr(C)
Density matrix
Scaling by the trace gives a valid quantum state. Its eigenvalues are the fractions of variance.
STEP 2
U = e^(2πiρ)
Unitary
A quantum operation whose phases equal the eigenvalues of ρ.
STEP 3
QPE
Phase estimation
t phase qubits read each eigenvalue to a resolution of 1 / 2t.
STEP 4
Measure
Read-out
Phase register gives λ. System register collapses to the principal component.
Qubit budget: 14 sensors are padded to 16 dimensions, which fit in 4 system qubits. With 8 phase qubits the circuit uses 12 qubits and resolves eigenvalues to 1/256 of the total variance.
Notes: This is the core idea from Lloyd, Mohseni and Rebentrost, 2014. Divide the covariance matrix by its trace and it has all the properties of a density matrix, the mathematical description of a quantum state. Its eigenvalues are now fractions of total variance. Build the unitary U from it. Quantum phase estimation reads the phases of U, and those phases are exactly the eigenvalues. When the phase register is measured, the system register is left in the corresponding eigenvector, which is the principal component.

## Slide 8: The phase-estimation circuit at the heart of the app
|0⟩ a0
|0⟩ a1
|0⟩ a2
ρ (4 qubits)
H
U
M
H
U2
M
H
U4
M
QFT†
m ≈ λ · 2t
eigenvector |v⟩
H Hadamard gates put the phase qubits into superposition.
U Controlled powers of U write the eigenvalue into the phases.
QFT† Inverse Fourier transform turns phases into a binary number.
Notes: Walk through the circuit left to right. Phase qubits start in zero and get Hadamard gates, creating a superposition of all counting states. Each phase qubit controls a power of U applied to the system register, which holds rho. This writes the eigenvalue into the phases of the phase register. The inverse quantum Fourier transform converts those phases into a binary number, and measurement reads it out. The app shows only three phase wires for clarity; the default is eight.

## Slide 9: What the simulation covers, and what it leaves out
Simulated exactly
Full state evolution through Hadamards, controlled U powers, inverse QFT and measurement
State preparation as a purification of ρ built from the data, with no eigendecomposition
Finite-shot measurement statistics for the phase register
Phase resolution limits set by the number of phase qubits
Not simulated
Density-matrix exponentiation from copies of ρ: U is built with expm instead
QRAM loading of the sensor data
Gate noise and decoherence
Real state tomography: eigenvectors are read directly, with a simple 1/√n noise model for finite shots
Notes: This slide matters for credibility. We simulate the phase-estimation circuit exactly: the state after every stage is computed with no approximation. What we do not simulate are the two expensive steps a real device would need: loading the data into a quantum state, and building U from many copies of rho. We build U with a matrix exponential on the classical computer. So we verify that the algorithm gives the right answer, and we make no claim about speed.

## Slide 10: From reduced coordinates to a health status
Distance from the healthy region
d2 = (z − m0)T S0−1 (z − m0)
Anomaly score between 0 and 1
A = 1 − exp(−ln 2.5 · d2 / d299)
z: the cycle in PC space. m0, S0: mean and covariance of healthy cycles. d299: the distance that contains 99% of healthy cycles, so A = 0.60 exactly at that boundary. The score is averaged over the last 5 cycles.
NORMAL
A below 0.60
Inside the healthy region.
EARLY DEGRADATION
A from 0.60 to 0.85
Leaving the healthy region; plan an inspection.
HIGH ANOMALY
A above 0.85
Far from healthy; act now.
Notes: After projection each cycle is a point in k-dimensional space. Healthy cycles from the fitting engines form a cloud; we describe it by its mean and covariance. The Mahalanobis distance measures how far a new point is from that cloud, taking its shape into account. The exponential map squeezes distance into zero to one, calibrated so the score is exactly 0.60 at the edge that contains 99 percent of healthy points. A five-cycle moving average stops single noisy readings from raising alarms. The thresholds 0.60 and 0.85 are design choices.

## Slide 11: The MATLAB application: seven tabs, one story
1 Data
Pick dataset and engine; see raw readings.
2 Sensor health
Any sensor over the engine's life.
3 Classical PCA
Scree plot and sensor loadings.
4 Quantum PCA
Circuit, phase histogram, eigenvalue table.
5 Engine health
Score over time and animated 3D health map.
6 Classical vs qPCA
Metric table and eigenvalue comparison.
7 What if?
Noise sweep and component sweep.
Always visible
Engine, status lamp and anomaly score in the header.
Notes: The app is a single MATLAB window. The header always shows the selected engine, its status lamp and its score. The left panel has the controls: dataset, engine, number of components, noise level, phase qubits and shots. The seven tabs follow the order of the method, so a demo simply moves left to right.

## Slide 12: Architecture: one pipeline, two PCA engines
C-MAPSS
loadCMAPSS
Preprocess
select, split, z-score
Classical PCA
eig of C
qPCA
phase estimation
Compare
6 metrics
Score
A(x)
Status
3 levels
Both branches return eigenvalues and eigenvectors in the same format, so projection, health model and scoring are shared. Numerical code lives in /core and is tested without the interface.
Notes: The same preprocessed data feeds both PCA methods. Their outputs have the same form, eigenvalues and eigenvectors, so everything downstream is shared: projection, health model, scoring, status. That is what makes the comparison fair. All numerical code sits in separate functions in the core folder and is tested without the user interface.

## Slide 13: Quantum versus classical is measured, not assumed
Eigenvalue error
relative difference from classical λ
Component fidelity
overlap |⟨v_c|v_q⟩| per component
Variance captured
by the first k components
Reconstruction error
on held-out engines
Anomaly AUC
healthy vs last 30 cycles, held-out
Run time
seconds, simulation only
Chart: qPCA eigenvalue error vs phase qubits (%)
| 6 qubits | 8 qubits | 10 qubits
Eigenvalue error (%) | 4.5 | 1.05 | 0.33
Development check on synthetic stand-in data (k = 3, exact shots). Not NASA results: run the app on FD001 and replace.
Notes: Six metrics compare the two methods. The chart shows a check from the development tests on synthetic stand-in data: the qPCA eigenvalue error falls as phase qubits are added, as theory predicts, because resolution is one over two to the t. These numbers are from synthetic data and only confirm the code behaves correctly. The results on NASA FD001 must be produced by running the app on the real files and inserted here.

## Slide 14: Two experiments the audience can run live
Sensor noise
How robust is qPCA when measurements get noisier?
Slider adds 0 to 50% noise relative to each sensor's spread
Pipeline is refitted at every level
Output: detection AUC for both methods and qPCA eigenvalue error
Number of components
How much can 14 sensors be compressed?
Spinner sets k from 2 to 10
Every tab updates immediately
Output: variance retained, reconstruction error and detection AUC against k
Notes: Both experiments are buttons in the app. The noise sweep reruns the whole pipeline at six noise levels and plots detection quality and eigenvalue error for both methods. The component sweep varies k from 2 to 10 and shows the trade-off: more components capture more variance and reconstruct better, but the healthy region becomes harder to estimate and detection does not necessarily improve.

## Slide 15: Limits we state openly
Simulation, not hardware
Runs on a classical computer and is slower than eig. No quantum advantage is claimed.
Labels use hindsight
The healthy window and failing class rely on the known failure time of each engine.
Chosen thresholds
0.60 and 0.85 are design choices and can be tuned for a fleet.
Single operating regime
FD001 and FD003 only. FD002 and FD004 need per-regime normalisation.
Notes: State these before anyone asks. The quantum algorithm runs on a classical simulator, so it is slower than ordinary PCA here and that is expected. Labels for healthy and failing use the known failure time, which is valid for evaluating on run-to-failure data but not available on a live engine. Thresholds were chosen, not derived. Only single-regime subsets are supported.

## Slide 16: Many sensors in, one health signal out
qPCA finds the dominant patterns, the reduced space exposes drift from healthy behaviour, and the app turns that into an early warning.
Next steps
Run on FD001 and record the comparison table
Repeat on FD003 (two fault modes)
Report noise and component sweeps
Try a gate-level circuit with noise
Notes: Close by restating the story in one sentence, then the next steps: produce the real FD001 results, extend to FD003, report the two experiments, and as a stretch goal replace the matrix exponential with a gate-level circuit and a noise model.